## Slide 1: Computer Networking

## Slide 2: Computer Networking
A computer network is a system that connects numerous independent computers in order to share information (data) and resources. The integration of computers and other different devices allows users to communicate more easily.
A computer network is a collection of two or more computer systems that are linked together. A network connection can be established using either cable or wireless media. Hardware and software are used to connect computers and tools in any network.
A computer network consists of various kinds of nodes. Servers, networking hardware, personal computers, and other specialized or general-purpose hosts can all be nodes in a computer network. Hostnames and network addresses are used to identify them.

## Slide 3: Components of a network
Node
Server
Client
Network hardware
Communication channel

## Slide 4: Nodes
A node is any physical device within a network of other tools that’s able to send, receive, or forward information. Modems, switches, hubs, bridges, servers, and printers are also nodes, as are other devices that connect over Wi-Fi or Ethernet.
Nodes within a computer network must have some form of identification, like an IP address or MAC address, for other network devices to recognize them. A node without this information, or one that's offline, no longer functions as a node.

## Slide 5: Server
a server is a piece of computer hardware or software that provides functionality for other programs or devices, called clients. This architecture is called the client–server model. Servers can provide various functionalities called services, such as sharing data or resources among multiple clients, or performing computation for a client.

## Slide 6: Client
Client: When we talk the word Client, it mean to talk of a person or an organization using a particular service. Similarly in the digital world a Client is a computer (Host) i.e. capable of receiving information or using a particular service from the service providers (Servers).
Advantages of Client-Server model:
Centralized system with all data in a single place.
Cost efficient requires less maintenance cost and Data recovery is possible.
The capacity of the Client and Servers can be changed separately.
Disadvantages of Client-Server model:
Clients are prone to viruses, Trojans and worms if present in the Server or uploaded into the Server.
Server are prone to Denial of Service (DOS) attacks.
Data packets may be spoofed or modified during transmission.
Phishing or capturing login credentials or other useful information of the user are common and MITM(Man in the Middle) attacks are common.

## Slide 7: Network Hardware
Basic hardware interconnecting network nodes, such as Network Interface Cards (NICs), Bridges, Hubs, Switches, and Routers, are used in all networks.

## Slide 8: Network Interface Card(NICs)
NIC (Network Interface Card): A network card, often known as a network adapter or NIC (network interface card), is computer hardware that enables computers to communicate via a network. It offers physical access to networking media and, in many cases, MAC addresses serve as a low-level addressing scheme. Each network interface card has a distinct identifier. This is stored on a chip that is attached to the card.

## Slide 9: Repeaters
Repeater: A repeater is an electrical device that receives a signal, cleans it of unwanted noise, regenerates it, and retransmits it at a higher power level or to the opposite side of an obstruction, allowing the signal to travel greater distances without degradation. Repeaters are necessary for cable lengths longer than 100 meters in some systems.

## Slide 10: Router
Routers are networking devices that use headers and forwarding tables to find the optimal way to forward data packets between networks. A router is a computer networking device that links two or more computer networks and selectively exchanges data packets between them. A router can use address information in each data packet to determine if the source and destination are on the same network or if the data packet has to be transported between networks.

## Slide 11: Communication channel
Communication channels are the medium that connects two or more workstations. Workstations can be connected by either wired media or wireless media. It is also known as a transmission medium. The transmission medium or channel is a link that carries messages between two or more devices.
Guided Media: In this transmission medium, the physical link is created using wires or cables between two or more computers or devices, and then the data is transmitted using these cables in terms of signals. They are of 3 types: Twisted-pair cable, coaxial cable, fiber-optic cable
Unguided Media: The unguided transmission media is a transmission mode in which the signals are propagated from one device to another device wirelessly. Signals can wave through the air, water, or vacuum. It is generally used to transmit signals in all directions. It is of various types: Microwaves, radio waves, satellite, infrared waves, laser.

## Slide 12: Types of network
PAN
LAN
WAN
MAN

## Slide 13: Personal Area Network(PAN)
Personal Area Network (PAN) is the computer network that connects computers/devices within the range of an individual person. As PAN provides a network range within a person’s range typically within a range of 10 meters(33 feet) it is called a Personal Area Network.
Advantages:
PAN is relatively flexible and provides high efficiency for short network ranges.
It needs easy setup and relatively low cost.
It does not require frequent installations and maintenance
It is easy and portable.
Needs fewer technical skills to use.
Disadvantages:
Low network coverage area/range.
Limited to relatively low data rates.
Devices are not compatible with each other.
Inbuilt WPAN devices are a little bit costly.

## Slide 14: Local Area Network(LAN)
Local-area Network. It is a computer network that covers a relatively small area such as within a building or campus of up to a few kilometers in size. LANs are generally used to connect personal computers and workstations in company offices to share common resources, like printers, and exchange information.
Advantages
It allows the sharing of costly resources like printers, scanners among all of the computers. Thus, it reduces cost in hardware purchases.
It also allows sharing of software, instead of purchasing the separately licensed software for each client in a network.
Data is stored on the server computer, which makes it easier to manage data and makes the data more secure, as it is stored at only one place.
Communication among the connected computers is easy and cheap as data and messages can easily be shared with the other computers connected across the network.
Local Area Network also provides the facility to share a single internet connection among all the LAN users.
Disadvantages
The initial setup costs of installing Local Area Networks is high because there is special software required to make a server.
Communication devices like an Ethernet cable, switches, hubs, routers, cables are costly.
LAN administrator can see and check personal data files as well as Internet history of each and every LAN user. Hence, the privacy of the users are violated
LANs are restricted in size and cover only a limited area

## Slide 15: Metropolitan Area Network(MAN)
MAN stands for metropolitan area network and it is basically a computer network that is made by connecting multiple LAN’S. MAN covers a geographical area which is known as the metropolitan area. It serves as a connection which is larger than LAN(Local Area Network) but smaller than WAN(Wide Area Network). It generally covers the area of a city.
Advantages :
MAN covers a larger area than LAN.
It has less implementation cost and it uses less resources.
It provides higher security than WAN.
It can cover area as large as a city.
MAN is a faster way to connect two fast LANs together. This is due to the fast configuration of links.
In some installation of MANs, users can share their internet connection. So multiple users can get the same high-speed internet.
Disadvantages :
MAN is not easily manageable as it becomes very complex.
It requires highly skilled people to look after it.
It requires more cables for connecting the LAN’s.
It has high management cost
It covers smaller area than WAN.
It is only used in metropolitan areas.

## Slide 16: Wide Area Network(WAN)
Wide area network is a computer network that covers a large geographical area consisting of two or more LANs or MANs. These networks are established with leased telecommunication circuits, in which two sides which are connected have routers that connect the LAN of both sides together in a network to facilitate communication.
Advantages of WAN
It covers large geographical area which enhances the reach of organization to transmit data quickly and cheaply.
The data can be stored in centralized manner because of remote access to data provided by WAN.
The travel charges that are needed to cover the geographical area of work can be minimized.
WAN enables a user or organization to connect with the world very easily and allows to exchange data and do business at global level.
Disadvantages of WAN
Traffic congestion in Wide Area Network is very high.
The fault tolerance ability of WAN is very less.
Noise and error are present in large amount due to multiple connection point.
The data transfer rate is slow in comparison to LAN because of large distances and high number of connected system within the network.